## Slide 1
ECE 4960
Spring 2017
Lab 3
Memory Usage in Computing
Edwin C. Kan
School of Electrical and Computer Engineering
Cornell University

## Slide 2: Memory Usage
Independent of CPU, MPU and GPU, your engineering and gaming applications will have execution speed related to your memory size: the memory required by your program and the memory the present platform has in various levels.
One major difference in programming languages: whether you control the memory (C, C++, Fortran, and assembly) or the memory is controlled for you (Java, Python and Matlab).
Collecting information is limited by the data transaction time on the channel:
  On-chip data bus (< 1ns)
  Off-chip memory data bus (RC lines < 10ns; serial RLC lines < 1ns)
  Off-PCB disk storage (> 1s setup, then parallelism from fast buffers used)
  Air (wireless)
  Internet (hubs and hops)

## Slide 3: Memory Disciplines
Machine optimism: Use your largest memory carefully, and let the platform take care of the rest.
Memory conscientious: Control the memory heap (C/C++) by malloc()/new() and free() for memory you use and do not use any more. Caveat: occasional fragmentation and garbage collection not under your control.
Memory micromanagement: Reserve most of your memory in a big vector, and centralize your memory usage by pointers

## Slide 4: Memory Bugs
Forgetting to allocate memory
Reading or writing to memory outside the allowed regions (this is the most common reason of a segmentation fault)
Dangling pointers which result in improper accesses to memory
Access being lost to allocated memory, resulting in irretrievable memory leak (now most platform returns the memory when the process is over, except in system programming).

## Slide 5: Memory in Computing
The memory technology:
  On-chip embedded memory (SRAM or DRAM) as cache
  Off-chip memory (DRAM)
  Off-chip nonvolatile random access memory (Flash)
  Off-chip nonvolatile disk memory (serial hard drive)
Future memory technology:
  Phase-change memory (PCRAM)
  Magnetic memory (on-chip) (MRAM, Spin-torque STT-RAM)
  Resistive RAM (ReRAM)
  Ferroelectric RAM (FeRAM)

## Slide 6: Memory in the Future
RW Speed
Energy (pJ/bit)
0.01
0.1
1
10
100
ns
ms
ms
Conv. Flash
FeRAM
FeFET
NC/Trap
Flash
Magnetic HDD
PCRAM
ReRAM
STT RAM
Access device and disturb issues
Scales poorly
Limited retention
SRAM/
DRAM
Limited endurance
No random access

## Slide 7: Memory Wall
Memory wall means the access speed of memory is the slowest part in a computing problem.
In addition to the memory technology (i.e., how fast we can access a memory cell), there is a mathematical rule for any memory array: Rent’s rule: the larger the memory array, the less is exposed in the array peripheral, and the slower the access time.
Even with future inventions, this is always true: The larger the memory array, the slower is your access speed. This includes our own brain.
It is therefore important to know the memory usage for your large computing problem. If it is automated, it is important to know the “performance optimization” scheme.

## Slide 8: Compiler Directives
Changing the –g flag to –O flag at compiling
Give compiler directives about how to optimize performance on the specific platform by querying the platform about memory sizes, instruction delay and cache structures (often in BIOS).
Perform profiling of each function, if not each line, to identify the present performance bottleneck.
Give further compiler directives on the data dependency so that vectorization and parallelization available on the specific platform can be fully utilized. Today’s computing platforms often have many “cores”, and vectorization and parallelization have become more common, as well as important.
Benchmark the performance on all of the available units and regression tests.

## Slide 9: Logic and Memory
Remember that computation is ONLY as fast as the available data.
If the data are not directly or speedily available, the CPU speed will NOT matter.
For typical CPU, the memory has the hierarchy of:
  Register, level-1 (L1) cache, level-2 (L2) cache, three of which are embedded on the chip,
  Main memory (often on PCB by SDRAM)
  Nonvolatile storage (NAND Flash as SSD or magnetic disk).
Data storage | System size (bits or bytes) | Instruction cycle delay
Registers | 256 – 1,024 bits | 1
L1 cache | 64 – 256 KB | 1 – 2
L2 cache | 2 – 64 MB | 3 – 8
Main off-chip memory | 4 – 16 GB | 10 – 30
Virtual memory on disk | 1 – 4 TB | 100 – 500 (buffer dependent)

## Slide 10: Data Locality
If your computing has to retrieve information often from virtual memory, surely it can be 100 times slower.
We need to compute with the most data locality: maximizing the use of data in Registers and L1 cache and minimizing data retrieval from virtual memory.
The cache cannot store all data due to size, but if the data are operated fully in each subset without too much swapping, we can still achieve much better computing efficiency.
When the compiler cannot decide on a data set that can fit into the available cache, cache thrashing can happen, where cache miss rate will be high and memory bus will be crowded.

## Slide 11: Data Dependency and Locality
Data locality can be separated to temporal and spatial locality. Both are important for efficient computing.
For temporal locality, we will keep the most often used data in cache by informing the compilers (global data by default will belong to this set).
For spatial locality, accessing the array stored sequentially will help greatly.
To optimize the use of data locality, it is important for the compiler to know the computing and memory access order, and plan computing accordingly.

## Slide 12: Vectorization and Parallelization
Vectorization belongs to the computing architecture category of SIMD (single instruction multiple data)
Parallelization belongs to the computing architecture of MIMD (multiple instruction multiple data).
Most memory architectures on common platforms support both SIMD and MIMD, but the memory can be distributed to each processing unit (distributed memory) or share a common large data memory (shared memory).
We often have a hybrid shared and distributed memory system in the modern multi-core CPU. Each OS uses the memory system differently.

## Slide 13: Hybrid Shared Memory
Shared
memory
CPU
CPU
CPU
CPU
Local Memory
CPU
CPU
CPU
CPU
Local Memory
CPU
CPU
CPU
CPU
Local Memory
CPU
CPU
CPU
CPU
Local Memory

## Slide 14: Computing Tasks in Parallel
In C++, this is often achieved by OpenMP (multi-processing) API:
#OMP parallel default (shared) private (local)
Thread assignment by parallelizing compilers:
  Spawning a parallizable region for multiple thread execution
  Dividing blocks of code among threads
  Distributing loops among threads
  Synchronization of threads for the non-parallelizable part.
The Amdahl’s law: The parallelizable fraction of the computing is f and the number of available processor is N, then the total speedup S in the most optimal way will be: